## Slide 1: My Projects
Aditya Sivaraj

## Slide 2: Telepresence
Bachelor’s Thesis Project

## Slide 3: Broad Objective
Sweden has a problem. They are not able to give adequate care to their senior citizens in nursing homes.
The whole department at this university were working on deploying robots to lighten the load of doctors and nurses at these facilities.
Their robot of choice at that point was Pepper Robot, by Softbank Robotics.

## Slide 4: My Objective
To develop a telepresence setup and implement it in the Pepper Robot.
This setup must be done without the use of their proprietary software, language or IDE. Because it must be available to all and should be versatile.
Hence, I was supposed to it in all open source code, including, Python, ROS Libraries, Qt, Gstreamer, etc.

## Slide 5: Summary of My Work
Created Video and Audio pipelines for both the respective data to be transmitted and received by the server and client, using the Gstreamer media library.
Setup controls for the client to be able to move the robot including the ability to set the angle and speed of movement, using ROS libraries.
Went around the manufacturer set firewalls of being able to access the robot’s root only via their proprietary software, using a modular program file in the proprietary language.
Made a basic Graphical User Interface (GUI) to put all my background work together for the client.

## Slide 6: Cart Pole – Model Predictive Control
Course Project

## Slide 7: Cart Pole Problem
A cart pole setup is a standard cart with 4 wheels with an inverted pendulum on top.
The goal of the problem is to let the pendulum go in an upright position and move the cart so that the pendulum never falls down.

## Slide 8: Model Predictive Control
It is suboptimal control algorithm that combines features of many other primitive control algorithms and is considered a significant improvement over the standard or popular Linear Quadratic Model.
The short hand version of the algorithm is this: at each and every discrete point defined in space, the model calculates the best possible trajectory or rather solves an optimization problem with respect to that point as if that is the starting point.

## Slide 9: Project Objective
The goal of the problem is to let the pendulum go at a random state and the cart should be controlled until a certain time so that the pendulum does not fall down.
Should use Model Predictive Control method to perform the control calculations. Should write code for the same.
Should print a rudimentary picture of the same for every time differential and final make a video out of all the frames.

## Slide 10: Summary of My Work
Set the initial global values and set the initial state to a random state subject to the constraints of the problem, including length of pendulum pole, masses, acceleration, number of states, number of inputs, horizon length and the time differential.
Let the cart go from aforementioned position and calculated the state and horizon at each time differential.
Was not able to put everything together as a video, but printed out every frame instead.

## Slide 11
A Frame from the Output

## Slide 12: Video Gesture Recognition
Course Project

## Slide 13: Project Objective
To create a module which recognizes gestures made by the user via a live video feed and performs actions based on the gesture. In this case, the actions perform media control.
Should use a Raspberry Pi 3B to take input of the live video feed and process it to recognize the gestures and perform media control actions based on it.

## Slide 14: Summary of My Work
Wrote code for media control and how to manage the gestures.
Tried writing code and training the ML model for gesture recognition using OpenCV libraries to get a series of images at all possible different angles for different gestures. The trained model did not work as well as expected due to a lack of enough sample size in different environments. Also, the computing power on the Raspberry Pi was not enough run the model trained by me.
Used an open source trained model for the required gestures and integrated it into my module.

## Slide 15: Self Balancing Robot
Summer Internship Project
Picture not from my project, but, is similar to this.

## Slide 16: Project Objective
The goal of this project is to make a cuboid structure about a foot tall with wheels on either side stand without falling.
The computer on the structure, and the sensors on it should foresee when it is about to fall and in which direction. After which, the bot will move in that direction to avoid the fall.

## Slide 17: Sensor Used
We used MPU6050 sensor (6-axis IMU), which is actually a combination of two sensors, namely, an accelerometer and a gyroscope. It also houses a Digital Motion Processor.
Accelerometer senses the angle of tilt in 3 axes.
The gyroscope in here is a 3-axis one which senses the orientation and the angular velocity.
The sensor gives a 6 value output with a 3 axis value from each sensor.

## Slide 18: Summary of Our Work
Built the setup with plastic boards, steel rods and toy car wheels.
Used Arduino to do the processing. Wrote code in C for the whole setup.
Interfaced MPU6050 sensor and the motors with Arduino.
Calibrated the sensor to the values that suited our project. This took the longest time, as the sensor was highly sensitive, and the six values did not coordinate well.

## Slide 19: Other Projects Done (Non-Exhaustive)
Path planning of a SCARA Manipulator using MATLAB.
Performed SLAM on a virtual quadrotor using MATLAB.